Caledonian Mining Cables

AS/NZS 1972:2006 Cables

Type 1 1.1/1.1KV Collectively Screened

� Applications .............................................................................................................

These collectively copper screened cables are used for wiring of machines, or between machines and equipment where PVC is suitable.

� Standards .................................................................................................................

AS/NZS 1972:2006

AS/NZS 1125

AS/NZS 3808

� Construction ............................................................................................................

Conductors: Stranded copper conductor.

Insulation: PVC.

Bedding: Polyester tape.

Collective Composite Screen (earth conductor): Tinned annealed copper braiding interwove with polyester yarn.

Sheath: PVC sheath.

Stranded Tinned Copper Conductor PVC Insulation

Filler

Polyester Tape

Collective Composite Screen PVC Sheath

�  Dimensions and Weight ..........................................................................................

| Number of Cores | Nominal Conductor Area | Strand Size | Insulation Thickness | Core Screen | Thickness of Sheath | Nominal Overall Diameter | Nominal Weight |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Strand Size | Area of Screen |  |  |  |
|  | mm� | No/mm | mm | mm | mm� | mm | mm | kg/100m |
| Type 1 � Collectively Screened |
| 2 | 1.5 | 30/0.25 | 0.8 | 0.20 | 2.3 | 0.8 | 9.2 | 12 |
| 3 | 1.5 | 30/0.25 | 0.8 | 0.20 | 2.5 | 0.8 | 9.7 | 15 |
| 4 | 1.5 | 30/0.25 | 0.8 | 0.20 | 2.6 | 0.8 | 10.5 | 18 |
| 6 | 1.5 | 30/0.25 | 0.8 | 0.20 | 3.4 | 0.8 | 12.6 | 25 |
| 16 | 1.5 | 30/0.25 | 0.8 | 0.20 | 5.1 | 1.0 | 18.7 | 55 |
| 30 | 1.5 | 30/0.25 | 0.8 | 0.25 | 8.8 | 1.3 | 24.6 | 96 |

www.caledonian-cables.co.uk  www.addison-cables.com	45